## Slide 1: Keil 환경설정

## Slide 2: Device 선택

## Slide 3: RTE 설정 (다음 화면과 같이 선택)
이것도 ITM으로 바꿔주기

## Slide 4: 컴파일러 I/O 설정 부분에 대한 설명
The Serial window accepts serial input and output data streams. The window displays serial output data received from a simulated CPU, while characters typed into a serial window are input to the simulated CPU. This allows testing a UART interface prior to having the target hardware.
The Debug (printf) Viewer is a special serial window that can exchange data with the microcontoller. For Cortex-M microcontrollers, the window displays printf-data received from the Instrumentation Trace Macrocell (ITM). To redirect output, refer also to Retarget Output via ITM, and Debug Access in the CMSIS documentation.

## Slide 5: main.c 파일 만들기
1. Source Group 1 마우스 우클릭
Add New Item 클릭
2. 이름 설정 Add 클릭

## Slide 6: Test (에러 없이 컴파일되면 환경설정 완료)
RTE 재설정 시

## Slide 7: hex 파일 만들기
Alt + F7
-> Options for Target의
Output 클릭
Create HEX File 선택
빌드 후 프로젝트 폴더의
Objects에 hex file 생성